Motion and Machine Unit Notes	  Name:

DO NOT LOSE!

Energy

  - Ability to do work

  - To cause something to change move or directions

  - Energy cannot be created or destroyed, but transferred from one form to another.

  - Energy quality is lost due to friction / force/ heat.

-From high quality energy to low quality energy.

Newton’s 1st Law of Motion

  - Every object in a state of uniform motion tends to remain in that state of motion unless an external force is applied to it.

- Inertia – Forces that resist to motion

Inertia

  - An object in motion tends to stay in motion unless acted upon by a force.

  - An object at rest tends to stay at rest unless acted on by a force.

- Friction - The resistance encountered when one body is moved in contact with another.

The four types of friction

  - Static friction- friction between two surfaces that are not moving past each other.

  - Sliding friction- the force that opposes the motion of two surfaces sliding past each other.

  - Rolling friction- the friction between a rolling object and the surface it rolls on.

  - Fluid friction- when an object is moving in liquid or gas.

Friction

•Slows an object down until it stops

•Produces heat

•Wears object down

- Aerodynamic: Designed or arranged to offer the least resistant to fluid flow.

- Hydrodynamic: A shape designed to move efficiently through the water.

3rd Law of Motion

  - For every action there is an equal and opposite reaction.

Newton’s 2nd Law

  - The relationship between an object's mass m, its acceleration a, and the applied force F is F = ma.

The net force on an object is equal to the mass of the object multiplied by its acceleration.

First law of energy (thermodynamics)

  - All energy is either kinetic or potential.

Potential Energy: (PE) The energy stored by an object as a result of its position

- Potential Energy is the energy of position. Objects that are elevated have a high potential energy.

- Kinetic Energy is the energy of motion

PE = MGH

- PE = Energy (in Joules)

- m = mass (in kilograms)

- g = gravitational acceleration of the earth (9.8 m/sec2)

- h = height above earth's surface (in meters)

Kinetic Energy

- The energy that matter has because of its motion and mass.

- where m = mass of object

- v = speed of object

- KE = Energy in Joules

- Don’t forget your order of operations.

- PEMDAS

- For KE, you must do exponents (E) before multiplying (M).  So square the velocity first, and multiply by half of the mass.

Kinetic energy

  - The energy that matter has because of its motion and mass.

  - The flow of electrons or charged particles called electrical energy are all examples of kinetic energy.

  - Amount of energy depends on both its mass and its velocity (speed).

- Mechanical Energy (ME) – Energy due to position and motion; sum of potential and kinetic energies. Includes heat and friction.

  - Just add Potential Energy + Kinetic Energy.

- Hydropower – Potential to Kinetic energy

- Speed = Distance over time

  - 80 km / 2 hrs = 40 km / hr

  - 80 miles / 2 hrs = 40 mph

- Velocity = Speed (distance / time) and direction.

- Acceleration = The rate of change in velocity.

- Acceleration = The final velocity – the starting velocity, divided by time.

- Deceleration – To slow velocity

- Momentum: A measure of the motion of a body equal to the product of its mass and velocity.

  - Momentum = Mass times velocity

- Amount of  Work (w) done depends on two things:

The amount of Force (F) exerted.

The Distance (d) over which the Force is applied.

- Equation for Work -  w = F x d

- Machines help us to do work!

- One Joule = N over a meter (N-m)

- Catapults - By the law of conservation of energy, the stored potential energy (U) is transferred into rotational kinetic energy (K), with some loss due to friction. U = K

- Trajectory – The path of flying object: the path that a projectile makes through space under the action of given forces such as thrust, wind, and gravity.

- Force: Is a PUSH or a PULL, that causes a change in the motion or shape of an object

  - Gravity, Electricity, Magnetism, and Friction

- F = w x d.

- W = F x d

Machines…

  - Transfer force from one place to another.

  - Change direction of a force.

  - Increase the magnitude of a force.

  - Increase the distance or speed of a force.

- Force is a quantity which is measured using the standard metric unit known as the newton

- One newton is the amount of force required to give a 1-kg mass an acceleration of 1 m/s/s.

Quick Cheat Sheet

- Potential Energy (PE) = mass kg * gravity (9.8) * height (Answer is in Joules)

- Kinetic Energy (KE) = ½ mass kg * Velocity squared (velocity * Velocity) (Answer is in Joules)

  - Square velocity first because it an exponent (PEMDAS)

- Mechanical Energy (ME) = Kinetic Energy + Potential Energy (Answer is in Joules)

- Speed – A Measure of motion, = Distance divided by time (Answer in meters per second m/s)

- Velocity – Rate of which an object changes its position. = Distance divided by time and direction. (Answer in meters per second and direction such North, East, South, West, or Northwest etc.)

- Acceleration – Change in velocity over time. Final Velocity minus the starting velocity divided by time. (Answer is in meters / sec/ and direction North, etc.

- Deceleration – Same as acceleration but the number will be negative.

- Mass – Amount of matter in an object.  On earth, weight and mass are the same. (Metric unit is the gram)

- Force =  (F=MA)  F = Mass (Weight on earth) * Acceleration (Answer is in newtons (m/s/s)

- Work – Force * Distance the force was applied (Answer is in newtons)